## Slide 1
Draft Proposal was prepared and submitted by S.Kuleshov (detector lab director at UTFSM, Valparaiso, Chile) on behalf of the group of Chilean Universities;
  Proposal was discussed and supported by representatives of
  - BNL - EK, CW
  - MEPHI (Russia) – Andrey Brandin;
  - IHEP (Russia) - Alexei Denisov;
  and our “Shashlykfriends in all kind of other places
It covers three years period and relies on funding from eIC R&D and home sources (~50/50)
“Shashlyk” electromagnetic calorimeter with improved energy, position and timing resolution for eIC

## Slide 2: “Shashlyk” electromagnetic calorimeter with improved energy, position and timing resolution for eIC
S.Kuleshov, Director of The Detector Laboratory of UTFSM, Valparaiso, Chile, 05/18/2017

## Slide 3: The proposal goals:
Current versions of “Shashlyk” calorimeter are optimal for combination with old read out with PMT. SiPM is a new trend in cheap photo detectors. This technology is being developed and is very promising. We propose to make a revision of “shashlyk” calorimeter design optimized for SiPM optical readout.
The detector will have a whole slew of new qualities. It will be performant, will have very good timing resolution and shower locating performance and will be optimized to specifications established by physics measurements at central rapidities at eIC.
We will build a number of proyotypes and beam test new detector and compare our measurements to Geant4 model .
To this aim we propose to create a collaboration of institutions interested in “shashlyk” technology under the umbrella of eIC Calorimetry Consortium.

## Slide 4: Prototypes
Take the minimal configuration with internal position sensitivity – “shashlyk” tower with 4 fibers, instrumented with MPPC and DAQ for each fiber. The transverse size of tower should be 15-20 mm taking into account optimal distance between fibers. It means that Moli’ere radius should be 15-20 mm. The scintillator plastic with thickness less than 1 mm could bring problem with scintillation light output. Taking into account this, we prefer to work with 1.5 mm scintillator plastic for minimization of lateral leakages. In this case 1.5 mm absorber from 80W20Cu alloy (or 2.6 mm of lead) is optimal. The price of 80W20Cu is not high, it is 50-80 $ per kilo. The 80W20Cu alloy could be machined without problems and we prefer this material to lead. The module with 27.5 X0 will have 80 80W20Cu and 80 scintillating plastic plates and length will be 240 mm. Estimated energy resolution will be about 12% (the stochastic term).
The prototype will be 5 x 6 towers. The 2x2 block of identical test towers will be located at the center of the prototype surrounded by leakage section which is just to insure total shower absorption. The central area will be used for precision configuration scanning. All towers in the cenral block will be instrumented with read out and DAQ for each MPPC+ fiber (120 channels).
We are going to produce 3 (or more) prototypes: the prototype with strait fibers, one prototype with spiral hole for fiber with 4 towers, one more prototype with spiral hole for fiber with 5 x 6 towers etc.

## Slide 5: The research program (test beam in BNL or/and NA64 CERN, cosmic ray test in Chile):
Scan with cosmic ray in horizontal and vertical positions. Get uniformity measurements. Show uniformity of light collection and the punch-through effect level.
Create Geant 4 model of the calorimeter based on the cosmic test.
Measure energy resolution with an electron beam from 0.2 GeV (?) to 30 GeV (?).
Make lateral scans with electron beam at 0.5(?)-30 GeV… energies.
Make lateral scan with muon beam.
Study rejection of hadrons from electrons with pion and electron beam.

## Slide 6: “Sashlik” calorimeter tower
80 W80Cu20 1.5 mm plates and 79 1.5 mm scintillator plastics
Full thickness is 169.5 mm.
It is 20X0. The weight of W80Cu20 is 0.682 kg
238.5
19

## Slide 7: Read out: 4 MPPC for 4 fibers without any fibers bundle.
PCB
3x3 SiPM (MPPC)
Light guide
A neutron fielding could be around MPPC

## Slide 8: The schedule of the work (3 years, today is Day “0”):
Production of small prototype with spiral holes for fibers July-September 2017
Production of prototype with strait fibers July-December 2017.
Production of hodoscopes July-December 2017.
Production of read out for hodoscopes July-October 2017.
Production read out for calorimeters July-Novemebr 2017.
Production of the large prototype with spiral holes for fibers October 2017-February 2018.
Assembling and test cosmic ray set up, January 2018.
Cosmic ray test of small prototype with spiral holes, January –February 2018
Cosmic ray test of the prototype with strait fibers, March-April 2018.
Cosmic ray test of the large prototype with spiral fibers, May-June 2018.
The transportation of prototypes to BNL, July-August 2018.
Test beam 2018 and 2019.

## Slide 9: Preliminary estimation of the budget for BNL&UTFSM collaboration.
Year 1: BNL - 95,000.00 USD + 1 month support of a student UTFSM - 26,600.00 USD
Year 2: BNL - 110,000.00 USD + 3 months support of an engineer
Year 3: BNL - 50,000.00 USD + 3 months support of an engineer
UTFSM (Chile) will pay for visits of Chilean’s researchers to BNL. The salary of researchers is not taken into account. Chile will pay salary of Chilean’s researchers.
Total: 255.00 USD of Project funds plus substantial institutional funding
New institutions are welcome!

## Slide 10: The End

## Slide 11: Reasons for this R&D:
Large scale SiPM production by HAMAMATSU, SenSel and other companies is pushing device prices down. Cost as low as 5$ for device with 1-4 mm2 sensitive area in SMD package looks realistic. It is comparable to price for 1mm diameter detector length WLS fiber with one end mirrowed. UTFSM has an experience with 16 WLS fibers IHEP/COMPAS Shashlyk modules. Coupling thoise fibers to individual SiPM’s passively ganged to a common readout will provide very compact and price competitive solution compared to classic “shashlyk” with bundled fibers. The detector will become insensitive to magnetic field. The solution is very attractive.
Implementation of as short as possible WLS fibers without bundling them kills punch-through pulses and reduces the cladding light contribution.
Connecting fiber-coupled SiPM’s to “individual” readout channels opens ways for rapidity controlled granularity and improve position resolution for photons, electrons and positrons and rejection of hadrons. It will also alleviate the needs for position correction with S-wave function for 2 D calorimeters like RCAL of EIC. It will help to discriminate low energy gammas from MIP particles (EIC). Timing measurements coupled to such a high granularity energy and position measurements could be very interesting for pointing cylindrical calorimeters.
“Shashlyk” with SiPM will be a cheapest (and easely tunable) option for the central EMC of eIC detector.